## Slide 1
Benchmarking Reinforcement Learning for Sustainable Energy Systems
Standard RL | Safe RL | Multi-Agent RL | Noise Robustness
Mehmet Koruturk Virginia Tech, RoleLab
Target: IEEE SmartGridComm 2026 | Deadline: June 19, 2026
EV Charging
Building HVAC
Cogeneration

## Slide 2
Project Overview & Scope
Research Question
How do different RL paradigms perform across diverse sustainable energy domains under realistic conditions?
Experimental Matrix: 3 Environments x 3 Paradigms x 3 Noise Types
Standard RL (PPO, SAC, TD3 via SB3)
EV Charging (54 stations, ACN-Data)
Building HVAC (RC thermal model)
Cogeneration (ONNX surrogate)
Safe RL (CMDP via OmniSafe)
EV Charging (54 stations, ACN-Data)
Building HVAC (RC thermal model)
Cogeneration (ONNX surrogate)
Multi-Agent RL (RLlib + PettingZoo)
EV Charging (54 stations, ACN-Data)
Building HVAC (RC thermal model)
Cogeneration (ONNX surrogate)

## Slide 3
Three SustainGym Environments
EV Charging
Source: ACN-Data (Caltech) Episode: 288 steps (24h, 5-min) Stations: 54 Action: Continuous [0,32] Amps Reward: profit - carbon - excess
Obs: Dict{timestep, departures, demands, MOER, forecasted_MOER} Safe RL cost: excess_charge * 100 MARL: 54 agents (1 per station)
Building HVAC
Source: EnergyPlus RC model Episode: 288 steps (24h, 5-min) Zones: Configurable (OfficeSmall) Action: Continuous [-1,1] per zone Reward: -(energy + temp_error)
Obs: Box(n+4) zone temps + weather + occupancy Safe RL cost: temp violations MARL: 1 agent per AC zone
Cogeneration
Source: ONNX surrogate model Episode: 96 steps (1 day) Components: 3 GTs + ST + aux Action: Mixed cont/discrete (15 keys) Reward: -(fuel + ramp + penalties)/1e7
Obs: Dict{Time, Prev_Action, ambient, targets, prices} Safe RL cost: dyn_cv / 1e7 MARL: 4 agents (GT1,GT2,GT3,ST)

## Slide 4
Noise Robustness Framework
Three Independent Noise Channels
Observation Noise
Applied after env step, before agent observes Simulates sensor uncertainty, forecast errors Scales: 0.0, 0.05, 0.10, 0.20, 0.40
agent sees noisy state
Action Noise
Applied before env processes action Simulates actuator imprecision, communication errors Scales: 0.0, 0.05, 0.10, 0.20, 0.40
env receives noisy action
Environment Noise
Applied in dynamics/reward computation Simulates real-world stochasticity, model mismatch Scales: 0.0, 0.05, 0.10, 0.20, 0.40
dynamics are stochastic
Key Question: Which noise type degrades performance most? (Hypothesis: env noise > obs noise > action noise)

## Slide 5
Publication Feasibility Assessment
STRENGTHS
+ 3 diverse environments spanning EV, building, cogen domains
+ 3 evaluation axes (standard RL + safe RL + MARL) — rare in literature
+ Structured noise decomposition (obs / action / env) — novel
+ Production-quality codebase (SB3 + OmniSafe + RLlib)
+ Realistic env models (ACN-Data, EnergyPlus RC, ONNX surrogate)
+ Extensive EVCharging results (15+ safe RL algorithms tested)
GAPS TO ADDRESS
- No non-RL baselines (rule-based, MPC) — CRITICAL
- Inconsistent experimental completeness across envs
- No documented statistical rigor (seeds, CIs)
- Missing domain-specific metrics beyond reward
- Env noise experiments incomplete
- No cross-axis (StdRL vs SafeRL vs MARL) comparison
VERDICT: Publishable at SmartGridComm with targeted improvements. Scope is right; execution needs completing.

## Slide 6
Literature Positioning & Gap
Existing Benchmarks
SustainGym (NeurIPS'23)
3 envs, basic RL baselines only
We extend with safe RL, MARL, noise
CityLearn (BuildSys'19)
Buildings only, MARL focus
We cover 3 domains, add safe RL
BOPTEST (JBPS'21)
Buildings only, includes MPC
We add RL benchmarking protocol
Sinergym (BuildSys'21)
EnergyPlus RL, single domain
We are multi-domain, multi-paradigm
Grid2Op / L2RPN
Transmission grid, different domain
Complementary; different scale
Our Unique Position
No existing benchmark covers EV + Building + Cogen under a unified protocol
No systematic safe RL benchmark across multiple energy domains
No structured obs/action/env noise decomposition for energy RL
No paper compares standard RL, safe RL, and MARL on the same environments

## Slide 7
Gap Analysis: What Must Be Done
CRITICAL
P0: Non-RL Baselines
Rule-based + optimization baseline per env. Answers 'why RL?'
CRITICAL
P0: Statistical Rigor
5+ seeds per experiment, bootstrap 95% CIs
CRITICAL
P0: Domain Metrics
Energy cost ($), CO2 (kg), constraint violation (%), comfort index, peak demand (kW)
CRITICAL
P0: Complete All Envs
Building & Cogen have gaps in noise sweeps, safe RL, and MARL training
HIGH
P1: Cross-Axis Comparison
StdRL vs SafeRL vs MARL on each env — the central deliverable table
HIGH
P1: Distribution Shift Test
Train clean, test noisy — most practical robustness evaluation
MEDIUM
P2: Noise Decomposition Ablation
Show obs vs action vs env noise have different impact profiles

## Slide 8
Current Experiment Completion Status
Experiment
EVCharging
Building
Cogen
Std RL (PPO/SAC/TD3)
Complete
Partial
Partial
Obs Noise Sweep
Complete
Partial
Partial
Action Noise Sweep
Complete
Partial
Missing
Env Noise Sweep
In Progress
Missing
Missing
Safe RL (OmniSafe)
Extensive
Early
Incomplete
MARL (RLlib)
APPO only
SAC only
PPO (100 iter)
Non-RL Baselines
Missing
Missing
Missing
Multi-seed (5+)
Unknown
Unknown
Unknown
Domain Metrics
Partial
Missing
Missing

## Slide 9
Proposed Contributions
C1
Unified Multi-Paradigm Evaluation Protocol
First benchmark comparing standard RL, safe RL, and MARL across multiple energy domains with standardized metrics
C2
Systematic Noise Robustness Analysis
Decomposed obs/action/env noise evaluation revealing which noise type impacts energy RL most
C3
First Safe RL Benchmark for EV Charging & Cogen
CMDP formulation with OmniSafe showing constraint violation vs. reward tradeoff (Pareto analysis)
C4
Cross-Domain MARL Comparison
Single-agent vs multi-agent across EV (54 agents), building (per-zone), cogen (4 agents)
C5
Open-Source Benchmark Suite
Reproducible training, evaluation, and reporting scripts with documented protocol and code release

## Slide 10
Novelty Assessment & Strengthening
Current Novelty: MODERATE
Environments are published (SustainGym NeurIPS'23). Algorithms are standard. Novelty must come from the benchmark protocol and insights it generates.
If We Add... We Can Claim...
Non-RL baselines (rule-based + LP/MPC)
"RL outperforms optimization under uncertainty"
Distribution shift experiments
"Policy robustness analysis under deployment conditions"
Cross-paradigm comparison table
"Safe RL reduces violations X% at Y% reward cost"
Open-source benchmark release
"Reproducible benchmark suite as community artifact"
Pareto analysis for safe RL
"Tunable safety-reward tradeoff characterization"

## Slide 11
Required Baselines
Every benchmark must answer: "Why use RL at all?"
Do-Nothing / Fixed [Effort: Trivial]
EV: Charge at max rate Building: Fixed thermostat setpoint Cogen: Nominal operating point
Rule-Based / Heuristic [Effort: Low]
EV: LLLF or proportional to demand Building: Deadband controller (+/- 1C) Cogen: Load-following proportional
Optimization (LP/MPC) [Effort: Medium]
EV: LP for min-cost scheduling Building: 1-step MPC with RC model Cogen: LP for fuel minimization
Minimum: Do-Nothing + Rule-Based for all 3 envs (feasible before deadline)

## Slide 12
Standardized Evaluation Protocol
Statistical Rigor
5 seeds per experiment (42-46) Bootstrap 95% confidence intervals Interquartile mean (per Agarwal et al. NeurIPS'21)
Domain-Specific Metrics
Energy cost ($) | CO2 emissions (kg) Constraint violation rate (%) | Peak demand (kW) Comfort / service quality index
Noise Robustness Protocol
For each {env x algo x noise_type x noise_level}: 5 seeds -> mean +/- 95% CI Distribution shift: train clean, test at noise={0.05,0.10,0.20,0.40}
Reporting Standards
Training curves: shaded IQR across seeds Bar charts with error bars for final performance Pareto fronts for safe RL (reward vs cost)
Required Paper Deliverables
Fig 1: Taxonomy diagram (3 envs x 3 paradigms x noise axes)
Fig 2: Training curves per env (shaded IQR)
Fig 3: Noise degradation curves (reward vs noise level by type)
Fig 4: Safe RL Pareto fronts (reward vs constraint cost)
Fig 5: MARL vs single-agent comparison bars
Table I: Env specs | Table II: Main results | Table III: Domain metrics | Table IV: Robustness

## Slide 13
Timeline to Submission (June 19, 2026)
Phase 1: Critical Fixes (Mar 3 - Apr 15)
Implement Do-Nothing + Rule-Based baselines (all envs)
Run all experiments with 5 seeds
Add domain-metric extraction to testing pipeline
Complete Building & Cogen std RL training
Phase 2: Core Experiments (Apr 15 - May 15)
Safe RL for Building & Cogen (3 algos x 5 seeds)
MARL training with sufficient iterations
Distribution shift experiments
Cross-paradigm comparison (StdRL vs SafeRL vs MARL)
Phase 3: Analysis & Writing (May 15 - Jun 12)
Generate all figures and tables
Write 6-page IEEE format paper
Internal review and revision
Code cleanup for public release
Phase 4: Submit (Jun 12 - Jun 19)
Final proofreading
Supplementary materials
Submit!

## Slide 14
Recommended Paper Structure (6-Page IEEE)
I. Introduction
0.75 pg
Problem statement, motivation, 5 contribution bullet points
II. Related Work
0.75 pg
RL for energy, safe RL, MARL, benchmarks with gap identification
III. Environments & Problem Formulation
1.0 pg
Table I (env specs), noise model formalization, CMDP formulation
IV. Experimental Setup
0.75 pg
Algorithms, hyperparameters, baselines, evaluation protocol, seeds
V. Results & Analysis
2.0 pg
Main results (Tables II-III), noise robustness, safe RL, MARL
VI. Discussion & Conclusion
0.75 pg
Key insights, limitations, future work, code release

## Slide 15
Key Research Questions & Expected Findings
Q1: Which algorithm wins?
Likely SAC for off-policy efficiency, PPO for stability under noise
Q2: Is safe RL worth the reward cost?
Quantify Pareto tradeoff: X% fewer violations at Y% reward reduction
Q3: Does MARL improve over single-agent?
Likely environment-dependent: EV charging may benefit, cogen may not
Q4: Which noise type matters most?
Hypothesis: env noise (distribution shift) dominates obs and action noise
Q5: Does RL beat non-RL baselines?
RL likely beats rule-based but may not beat MPC in low-noise settings

## Slide 16
Summary & Next Steps
The benchmark scope (3 envs x 3 paradigms) is strong and fits SmartGridComm
Critical gaps: non-RL baselines, statistical rigor, domain metrics, complete experiments
Novelty is moderate but can be strengthened with protocol + insights framing
Timeline is tight but feasible: 3.5 months to June 19 deadline
Priority: baselines > multi-seed > complete experiments > write paper
Immediate Actions
1. Implement Do-Nothing + Rule-Based baselines this week
2. Set up 5-seed runs for all completed experiments on ARC
3. Add domain-metric extraction to stdrl_testing.py
4. Queue remaining Building & Cogen experiments on ARC